## Slide 1
1
HIKMICRO FIREFIGHTING
THERMAL CAMERAS
INTRODUCTION
INDUSTRIAL PRODUCT | 2023.Q3
Thermal camera for observing in total darkness and smoke.
Notes: Compact Explosion Proof Thermal Camera for use in Hazardous Areas

## Slide 2: PRODUCT CATEGORY
Acoustic
Thermal
PRODUCT CATEGORY
Handheld
Fixed
Software
Firefighting
New
Explosion-proof
New
Acoustic
New

## Slide 3
CONTENTS
01 FB21
Compact And Reliable Thermal Camera For Observing In Total Darkness And Smoke.
02 FT31

## Slide 4
FB21- Overview
Basic Parameters |  | FB21
Infrared Image | IR Resolution | 256 × 192 (49,152 pixels)
 | NETD | < 40 mK (@ 25 °C, F#=1.0)
 | Image Frequency | 25 Hz
 | Field of View (FOV) | 37.2° × 50.0°
 | Min. Focusing Distance | 0.3 m (0.98 ft)
 | Focus Mode | Focus Free
Image Display | Visual Camera | 1600 × 1200 (2 MP)
 | Display | 240 × 320 Resolution, 3.2”LCD Screen
 | Color Palettes | Basic, Black Hot, White Hot, Fire Detection, Rescue, Hot Area, Cold Area, Building
Measurement and Analysis | Object Temperature Rang | -20°C to 550°C (-4°F to 1022°F)
 | Accuracy | Max. (± 2°C/3.6°F, ± 2%), for ambient temperature -20°C to 50°C (-4°F to 122°F) and object temperature above 0°C (32°F)
General | LED Light | Yes
 | Battery Type | Rechargeable Li-ion battery
 | Protection Level | IP65
 | Drop Test Height | 2 m (6.56 ft)
 | Working Temperature Range | Up to 10 minutes for ambient temperature -10°C to 90°C (14°F to 194°F); up to 2 minutes for ambient temperature -10°C to 115°C (14°F to 239°F)
 | Weight | Approx. 380 g (0.84 lb)
The HIKMICRO FB21 is a compact, reliable, firefighting thermal camera designed for firefighters to observe in total darkness and smoke, helping to save lives, protect property, and keep firefighters safe.
Features like dual cameras, LED flashlights, easy-to-navigate buttons, and a temperature range of up to 550°C (1022°F) help you work effortlessly in harsh environments. 8 color palettes for you to choose from, which satisfy most application scenarios.

## Slide 5
FB21– Form Factor
Thermal Lens， View the thermal image
Visual Lens, View the optical image
Wrist Strap Attachment Point and Tripod Mount
240 × 320 Resolution, 3.2”LCD Screen
LED Light
Trigger

## Slide 6
The HIKMICRO FB21 is a rugged, compact, high-quality thermal imaging camera designed for firefighters to observe in total darkness and smoke, helping to save lives, protect property, and keep firefighters safe.
FB21- Compact And Reliable
3.2” Color LCD
View the details of your images on the large, class-leading LCD screen
3.2”
256
High Image Quality
Features a highly sensitive (NETD < 40 mK) VOx detector, along with optimized image enhancement algorithms to provide clear thermal images.
Rugged & Durable Design
IP65 rated for protection against water and dust.
Featuring 2-meter (6.56ft)drop protection, suitable for harsh environment.
IP65

## Slide 7
FB21- For Observing In Total Darkness And Smoke
Working Temperature Range:
Up to 10 minutes for ambient temperature -10°C to 90°C (14°F to 194°F)
up to 2 minutes for ambient temperature -10°C to 115°C (14°F to 239°F)
For Smoke Systems
For Fire Rescue
For Building
FB21
Object Temperature Range: -20°C to 550°C (-4°F to 1022°F)
Notes: 工作温度范围
检测物体温度范围

## Slide 8
FB21- For Observing In Total Darkness And Smoke
8 color palettes give different image display options.
Among the palettes designed for firefighting, it allows you to make quick inspections in harsh environments.
Basic
For initial fire attack and rescue operations; colors represent temperature.
Fire Detection
For scenes with higher background temps where open flames are present, particularly in structural fires.
Rescue
For use with lower temperature situations, such as initial rescue efforts after traffic accidents, searches in wooded areas, etc.
Different palettes, corresponding to different Isotherm, with colors varying from yellow, orange, to red, help to quickly target temperature zones.
For example in basic mode:
Yellow coloring 150°C to 350°C;
Orange coloring 350°C to 550°C;
Red coloring >550°C
Notes: 用于在漆黑和浓烟中观测

## Slide 9
FB21- For Observing In Total Darkness And Smoke
8 color palettes give different image display options.
Among the palettes designed for firefighting, it allows you to make quick inspections in harsh environments.
Black &White
Same representations of temperature as the Basic mode, but in grayscale.
Hot Area
Used for finding hotspots. The hottest 20% of the scene is colored red.
Cold Area
Used for finding cold spots. The coldest 20% of the scene is colored blue.
Building
Used to detect temperatures in buildings such as mechanical, plumbing and electrical structures,etc.

## Slide 10
FB21- More Features
Thermal
Fusion
PIP
Visual
4 Images Modes
Thermal, Fusion, PIP and Optical modes to suit your preferred view.
25 Hz Fast Image Frequency
25 Hz fast image frequency delivers smooth video while panning across scenes or viewing moving targets.
Durable and Rechargeable Batteries
Built-in 3350mAh Li-Ion rechargeable battery allow the camera up to 6 hours of continuous operation.
The HIKMICRO FB21 is a rugged, compact, high-quality thermal imaging camera designed for firefighters to observe in total darkness and smoke, helping to save lives, protect property, and keep firefighters safe.
LED Flashlight
The LED flashlight allows you to work safely in dim or dark environments.

## Slide 11: FB21- Scope Of Delivery
Thermal Camera with Wrist Strap
Power Supply
International Use Plugs (US/EU/UK/AU/CN) for Power Supply
USB 2.0 A to USB Type-C Cable
Calibration Certificate
Quick Start Guide
Calibration Certificate
Charger and International Adapters
Thermal Camera with Wrist Strap
USB Cable
Quick Start Guide
Compact thermal camera for observing in total darkness and smoke.

## Slide 12
FT31 - Overview
Basic Parameters |  | FT31
Infrared Image | IR Resolution | 384 x 288 (110,592 pixels)
 | NETD | < 35 mK (@ 25°C, F#=1.0)
 | Image Frequency | 60 Hz
 | Field of View (FOV) | 54.1°×40.2°
 | Min. Focusing Distance | 1 m (3.28 ft)
 | Focus Mode | Focus Free
Image Display | Display | 800 × 480 Resolution, 4.3" LCD Screen
 | Digital Zoom | N/A
 | Color Palettes | Basic, Black Hot, White Hot, Fire Detection, Rescue, Hot Area, Cold Area, Building
Measurement and Analysis | Object Temperature Rang | -20°C to 1200°C (-4°F to 2192°F)
 | Accuracy | Max. (± 2°C/3.6°F, ± 2%), for ambient temperature 15°C to 35°C (59°F to 95°F) and object temperature above 0°C (32°F)
Data Storage and Communication | Storage Media | Built-in 32 GB flash memory
 | Video File Format | MP4 video
General | Battery Type | Interchangeable and rechargeable Li-ion battery
 | Protection Level | IP67
 | Drop Test Height | 2 m (6.56 ft)
 | Working Temperature Range | -20°C to 50°C (-4°F to 122°F) 80°C(176°F)，40min 150°C(302°F)，15min 260°C(500°F)，7min
 | Weight | Approx. 1022g (2.25 lb)
The HIKMICRO FT31 is a high-performance firefighting thermal camera designed for firefighters to observe in total darkness and smoke, helping to save lives, protect property, and keep firefighters safe. Features like object details enhancement, easy-to-navigate buttons and a working temperature range of up to 260°C(500°F) help you work effortlessly in harsh environments. 8 color palettes for you to choose from satisfy most application scenarios.

## Slide 13
Lanyard Mounting Points
Neck Strap Mounting Points
Interface Cover For USB Type-C
Thermal Lens
FT31– Form Factor
Keypad Controls for use with Gloves or PPE
800 × 480 Resolution, 4.3" LCD Screen
In-truck Charger Contacts
Trigger
Interchangeable and Rechargeable Li-ion Battery System for up to 12 hours of runtime

## Slide 14
FT31– Form Factor
Accessory Installation
Neck Strap
Lanyards
①Lanyard ②Retractable Lanyard

## Slide 15
FT31 – High-performance Thermal Camera
The HIKMICRO FT31 is a high-performance thermal imaging camera designed for firefighters to observe in total darkness and smoke, helping to save lives, protect property and keep firefighters safe.
60Hz
384
High Image Quality
Features a highly sensitive (NETD < 35 mK) VOx detector, along with ODE(Object Details Enhancement) to provide clear thermal images.
Rugged & Durable Design
IP67 rated for protection against water and dust.
Featuring 2-meter (6.56ft)drop protection, suitable for harsh environment.
IP67
60 Hz Fast Image Frequency
60 Hz fast image frequency delivers smooth video while panning across scenes or viewing moving targets.

## Slide 16
FT31- For Observing In Total Darkness And Smoke
Working Temperature Range:
-20°C to 50°C (-4°F to 122°F); 80°C(176°F)，40min; 150°C(302°F)，15min; 260°C(500°F)，7min
For Fire Rescue
For Building Construction
Object Temperature Range: -20°C to 1200°C (-4°F to 2192°F)
FT31
For Firefighting/ Smoke Systems

## Slide 17
FT31- For Observing In Total Darkness And Smoke
8 color palettes give different image display options.
Among the palettes designed for firefighting, it allows you to make quick inspections in harsh environments.
Basic
For initial fire attack and rescue operations; colors represent temperature.
Fire Detection
For scenes with higher background temps where open flames are present, particularly in structural fires.
Rescue
For use with lower temperature situations, such as initial rescue efforts after traffic accidents, searches in wooded areas, etc.
Different palettes, corresponding to different Isotherm, with colors varying from yellow, orange, to red, help to quickly target temperature zones.
For example in basic mode:
Yellow coloring 150°C to 600°C;
Orange coloring 600°C to 1200°C;
Red coloring >1200°C

## Slide 18
FT31- For Observing In Total Darkness And Smoke
8 color palettes give different image display options.
Among the palettes designed for firefighting, it allows you to make quick inspections in harsh environments.
Black &White
Same representations of temperature as the Basic mode, but in grayscale.
Hot Area
Used for finding hotspots. The hottest 20% of the scene is colored red.
Cold Area
Used for finding cold spots. The coldest 20% of the scene is colored blue.
Building
Used to detect temperatures in buildings such as mechanical, plumbing and electrical structures,etc.

## Slide 19
High Capacity Storage
Built-in 32 GB flash memory it can store at least 100,000 images.
FT31 – More Features
4.3" LCD Screen
View the details of your images on the large, LCD screen. With 1x, 2x, 4x digital zoom provides more image details.
Start-up time: 5 seconds (with IR image), 10 seconds (with OSD)
Fast Startup
Interchangeable Battery System
Includes 2 interchangeable Li-ion batteries and a dual bay charger to provide you with up to 12 hours of operation.

## Slide 20
FT31 - Scope Of Delivery
Accessories | Items | Quantity
Device | Thermal Imager | 1
Straps | Neck Strap | 1
 | Lanyard | 1
 | Retractable Lanyard | 1
Batteries and Power | Interchangeable and Rechargeable Li-ion Batteries | 2
 | Power Supply for Battery Charger | 1
 | Two-bay Battery Charger | 1
 | International Use Plugs (US/EU/UK/AU) for Power Supply | 4
Cables | USB 2.0 A to USB Type-C Cable | 1
Cases and Pouches | Hard Carrying Case | 1
Manuals | Calibration Certificate | 1
 | Quick Start Guide | 1

## Slide 21
See the World in a New Way
THANK YOU
HIKMICRO Thermography
HIKMICRO Thermography
hikmicro_thermography
HIKMICRO
Official Website: www.hikmicrotech.com/en/industrial/
Public Email Address: info@hikmicrotech.com